## Slide 1: Problem Description
Using Reinforcement Learning (RL) to train a cubesat to follow a pre-defined relative orbit about a target object
  Proximal Policy Optimization (PPO) learning algorithm is used to develop a control policy to track a reference trajectory
  Cubesat can issue thrust at each timestep in the simulation
System parameters
  Cubesat mass: 3 kg
  Thrust limit: +/- 0.02 (no restriction on duty cycle)
Training parameters
  Three policies trained simultaneously, each for a different reference orbit
    10 m, 15 m, 20 m (each circular about target)
    Reference orbit period: 6 minutes
  Training performed in batches of 10 for 5,000 iterations
    Total of 50,000 orbits simulated per cubesat

## Slide 2: Actions and Observations
Actions
  Torque for each manipulator joint
Observations
  End effector errors (position, orientation)
  Joint angles
  Joint rates

## Slide 3: Reward Function
Total reward is the sum of 3 components
  position error, velocity error, control effort
  Reward is issued on each time step of the simulation
Position and velocity rewards (R) are positive 1.0 when the errors (xe) are below a tolerance (tol) then exponentially decrease when above the tolerance
  Exponential rewards configured through scale factor and multiplier parameters
Control reward is a simple linear multiplier on the total thrust (F)

## Slide 4
Cubesat | r (m) | X (m) | Y (m) | Z (m) | xDot (m/s) | yDot (m/s) | zDot (m/s)
1 | 10 | -10 | 0 | 0 | 0 | -0.1745 | 0
2 | 15 | -15 | 0 | 0 | 0 | -0.2611 | 0
3 | 20 | -20 | 0 | 0 | 0 | -0.3491 | 0
Cubesat Initial Conditions
2D orbits
Orbit Period = 6 minutes
Performance after 10,000 training orbits
Performance after training complete 50,000 orbits